## Slide 1: Tutorial: Isocenter shifting image-guidance in SlicerRT
Csaba Pinter1, Andras Lasso1, An Wang2, Gregory C. Sharp3, David Jaffray2, and Gabor Fichtinger1
1Laboratory for Percutaneous Surgery, Queen’s University, Kingston, ON, Canada 2University Health Network, Toronto, ON, Canada
3Department of Radiation Oncology, Massachusetts General Hospital, Boston, MA, USA

## Slide 2
Learning objective
This tutorial demonstrates how to perform a radiation therapy research workflow using the SlicerRT toolkit:
Isocenter shifting image-guidance
Isocenter shifted and uncorrected DVH of the PTV

## Slide 3
Material
Dataset available on the Slicer Training page: https://www.slicer.org/wiki/Documentation/Nightly/Training#Slicer4_Radiation_Therapy_Tutorial
Supported platforms: Windows, Mac OSX, Linux
  32-bit is not supported!

## Slide 4
Overview
Install SlicerRT extension
Load data from DICOM and nrrd files
Perform rigid registration on CT images
Transform day 2 dose volume
Accumulate dose distributions
Compute dose volume histogram
+1. Create isodose lines and surfaces
+2. Compare dose distributions using gamma

## Slide 5
1/1. Install 3D Slicer
Download latest 3D Slicer from http://download.slicer.org
Follow the usual steps to install an application
  Different for each operating system

## Slide 6
1/2. Install SlicerRT extension
or

## Slide 7
1/3. Install SlicerRT extension

## Slide 8
2/1. Unpack tutorial datasets
Find the dataset you downloaded named SlicerRT_WorldCongress_TutorialIGRT_Dataset.zip
Unpack it to a local folder of your choice
  Different for each operating system
Notes: ENT RANDO phantom dataset and simulated day 2 CT and dose

## Slide 9
2/2. Import planning DICOM data
You’ll be prompted for database folder here
Drag&drop folder named EclipseEntPhantomRtData onto Slicer

## Slide 10
Note
If not importing via drag&drop, DICOM data can be imported and loaded from the DICOM browser that can be opened from the toolbar

## Slide 11
2/3. Load planning study
1. Click patient ‘RANDO ENT’
2. Click ‘Load’

## Slide 12
2/4. Change shown volumes
2. Link slices together
3. Choose shown volume to CT: ‘2: ENT IMRT’
1. Open slice controls

## Slide 13
2/5. Tweak display
1. Reset 3D view
2. Manipulate 3D view
Rotate with left button
Zoom with right button
3. Adjust window/level
Click&drag left button
4. Navigate slice view
Change slice by scrolling
Zoom with right button
Pan with middle button (Shift+click&drag on Mac)

## Slide 14
2/6. Explore loaded data
Subject hierarchy:
Explore data in tree view
Show/hide branches clicking the eye buttons
Access options by right click

## Slide 15
2/7. Load day 2 data
Drag&drop folder named EclipseEntComputedDay2Data onto Slicer

## Slide 16
Note
Data type selection dialog does not appear if you drag&drop files rather than folders, as files will be handled as non-DICOM
Non-DICOM data can be also loaded in the dialog that appears after clicking
Data can be saved using

## Slide 17
2/8. Add day 2 non-DICOM data to subject hierarchy
1. Right-click the patient
2. Create child study
3. Right-click (or double-click) new study item
4. Rename to ‘Day 2’

## Slide 18
2/9. Add day 2 non-DICOM data to subject hierarchy
1. Drag&drop ‘2_ENT_IMRT_ Day2’ on the study ‘Day 2’
2. Do the same with ‘5_RTDOSE-Day2’
Note: You can select both nodes while holding the Control/Cmd or Shift button, then drag&drop both at the same time

## Slide 19
2/10. Convert day 2 dose volume actually a dose

## Slide 20
3/1. Register CT volumes
Set up parameters as shown: 2. Choose ‘2: ENT_IMRT’ as fixed image 3. Choose day 2 CT ‘2_ENT_
IMRT_Day2’ as moving image 4. Create linear transform
and rename it to
Transform_Day2ToDay1_Rigid 5. Choose ‘Rigid (6 DOF)’
6. Click ‘Apply’
1. Go to module Registration / General Registration (BRAINS)

## Slide 21
Note
You can also initiate registration from subject hierarchy (alternative way for previous step):

## Slide 22
3/2. Explore volume differences
2. Set volume on foreground layer
3. Change foreground opacity
Optional: Set the same W/L in Volumes module
1. Open slice layers ‘>>’

## Slide 23
4/1. Clone dose volume
1. Switch to Subject hierarchy
2. Select ‘Clone node’ in context menu for day 2 dose
3. Rename it to ‘5_RTDOSE_Day2 Rigid’
To be able to compare the non-registered (= uncorrected) and the registered (= isocenter shifted) results.

## Slide 24
4/2. Transform cloned dose volume
1. Double-click transform column of cloned dose
2. Click ‘None’ to open drop-down

## Slide 25
Note
1. Double-click transform column of study
2. Click ‘None’ to open drop-down
We can transform the whole study too if we want to transform multiple objects (an alternative way for previous step):

## Slide 26
5/1. Accumulate dose distributions
1. Go to module Radiotherapy / Dose Accumulation
2. Choose reference, then planning and day 2 dose volumes
3. Create output volume
4. Click ‘Apply’

## Slide 27
5/2. Accumulate dose distributions
1. Uncheck day 2 dose volume
3. Create new output volume
4. Click ‘Apply’
2. Select registered day 2 dose

## Slide 28
6/1. Compute DVH for unregistered
1. Go to module Radiotherapy / Dose Volume Histogram
2. Choose unregistered accumulated dose
3. Choose ‘3: RTSTRUCT: ENT’
4. Click ‘Compute DVH’
Optional: Choose individual structures to speed up computation

## Slide 29
6/2. Compute DVH for registered
1. Choose registered accumulated dose
2. Click ‘Compute DVH’
3. Click ‘Show all’
DVH curves appear

## Slide 30
6/3. Quantify improvement

## Slide 31
6/4. Visualize improvement
Zoom using left mouse button click&drag
(Reset zoom: double left-click)

## Slide 32
Congratulations!
Thanks for attending!

## Slide 33
Appendix: Optional steps for IGRT

## Slide 34
Optional 1/1. Isodose lines/surfaces
1. Choose Radiotherapy / Isodose module
2. Click Apply
3. Select ‘5_RTDOSE_Day2’ volume as Dose volume
4. Click Apply
3. Select ‘5: RTDOSE: BRAI1’ volume as Dose volume

## Slide 35
Optional 1/2. Visualize isodose lines
1. Switch to Subject Hierarchy
2. Turn on and off visualization of isodose line and surface groups by clicking the eye icon next to the parent node
Note: Display volumes in the 2D viewers by clicking the volume show/hide icon next to the volumes

## Slide 36
Optional 1/3. Isodose lines/surfaces

## Slide 37
Optional 2/1. Compare dose volumes using gamma comparison
1. Go to module Radiotherapy / Dose Comparison
2. Set input volumes you want to compare
3. Create new output gamma volume
4. Click ‘Apply’

## Slide 38
Optional 2/2. Evaluate improvement
Plan dose vs
Uncorrected Day 2 dose
Plan dose vs
Corrected Day 2 dose