## Slide 1: SlicerRT 3DSlicer extensions for radiotherapy research
Andras Lasso1, Csaba Pinter1, Kevin Wang2, Steve Pieper3, Greg Sharp4, and Gabor Fichtinger1
1Laboratory for Percutaneous Surgery, Queen’s University, Canada; 2University Health Network, Toronto, ON, Canada; 3Isomics; 4Massachussetts General Hospital, Boston, MA, USA

## Slide 2: SparKit project overview
Goal: provide open-source platform for translational clinical research, mainly cancer
Funding: about $700k/year (including matching funding), for 5 years, started in 2011
PI & co-PI: Gabor Fichtinger (Queen’s), David Jaffray (Toronto UHN), Terry Peters (Robarts)
Themes:
  SlicerRT: radiotherapy toolkit for 3D Slicer
  SlicerIGT: Image-guided therapy with 3D Slicer

## Slide 3: SlicerRT theme overview
Motivation: commercial treatment planning software are costly and closed, existing research tools & applications (CERR, PLUNC, dicompyler, ...) are limited
Goal: provide a free, open-source software platform for radiotherapy (RT) research
Approach:
  Use 3DSlicer as platform
  Implement DICOM-RT data import: mapping RT data structures to existing 3DSlicer data types
  Utilize existing 3DSlicer functionalities: registration, visualization, ...
  Develop missing RT-specific functionalities: DVH analysis, ...
  Export results in DICOM-RT (for importing into treatment planning system) or for further analysis (in Matlab, ...)

## Slide 4: SlicerRT extension for 3D Slicer
Collection of RT-specific modules
Distributed as a 3D Slicer extension: can be downloaded, installed, upgraded using the extension manager in Slicer

## Slide 5: DICOM-RT import module
Integrated into core DICOM import module
Mapping to existing structures:
  Structure sets -> each structure set is imported as either a model (for planar contour ROI) or a fiducial point (for point ROI)
    Structure set color -> model color
    Structure set name -> model node name
    Slice thickness (for planar contour) -> ribbon filter width
  Dose map -> scalar volume
    dose unit -> MRML node attribute
  RT image -> read as regular volume
  Planning CT, MR, etc. -> read as regular volume
  RT plan -> only isocenter positions imported
Source code: https://www.assembla.com/code/sparkit/subversion/nodes/trunk/SlicerRt/src/DicomRtImport

## Slide 6: Imported structure sets, dose map, CT

## Slide 7: Imported contours can be converted to closed surface models, displayed on the image slices, transformed, etc.
Imported contours (surface model, ribbons)
Contours converted to labelmap
Contours converted to closed surface

## Slide 8: Dose Volume Histogram module

## Slide 9: Dose metrics
Available metrics:
Total volume
Min, max, mean dose
V metrics: for user-defined levels, results in cc and %
D metrics: for user-defined levels in cc and %
Values can be exported to CSV file for further analysis.

## Slide 10: DVH plot
Displayed on screen; zoom, trace, etc. available
Bin values can be exported CSV file

## Slide 11: Dose accumulation module
Computes a weighted sum of selected dose volumes.

## Slide 12: SlicerRT development plan
Planned high-level features:
Extensive validation, comparison of computation results to commercial TPS software
Dose volume comparison (gamma, etc.)
Dose volume histogram comparison
Structure set comparison
Isodose curve and surface display
DICOM-RT export
Matlab bridge: data exchange with Matlab, running Matlab scripts
Detailed plan: https://www.assembla.com/spaces/sparkit/tickets

## Slide 13: More details
SparKit: https://www.assembla.com/spaces/sparkit/
SlicerRT: https://www.assembla.com/spaces/sparkit/wiki/SlicerRt
Questions, feature requests contact: Andras Lasso (lasso@cs.queensu.ca)

## Slide 14: Appendix

## Slide 15
Adaptive radiotherapy for head and neck cancer (http://www.na-mic.org/pages/DBP:Head_and_Neck_Cancer)
  Funded by NA-MIC, 2010-2013
  PI: Greg Sharp (MGH, Boston, MA)
  4 researchers, software engineers
NA-MIC collaborations in preparation (http://www.na-mic.org/Wiki/index.php/ Events:Computational_Methods_for_Radiation_Oncology)
All these related are coordinated (through teleconferences, meetings at NA-MIC project weeks, etc.), collaborative efforts.
SlicerRT uses Plastimatch internally for certain computations.
Other RT related Slicer projects
Notes: Relatively new effort, but its funding is secured for a couple of years
SparKit: create hardware, software, imaging and database systems to enable oncologists to adapt radiation to each individual patient and their response during the course of therapy.

## Slide 16: CERR vs. SlicerRT
 | CERR | 3D Slicer & SlicerRT
 | http://cerr.info/features.php | 
Multimodality Image Fusion | Yes | Yes
PET Import | Yes | Yes
SPECT Import | Yes | Yes
MR Import | Yes | Yes
Visualization tool to compare Scan and Dose. | Yes | Yes
DICOM Export and Import(Optional) options. | Yes | WIP
Conversion of RTOG format treatment planning archives or DICOM-RT into the Matlab-readable CERR format. | Yes | Not planned
Interactive CERR command line help. | Yes | Yes
DICOM RT html help documentation is provided under help menu. | Yes | Yes (on-line documentation)
Translation of structures in x,y,z. | Yes | Yes
Captures the snap shot of CERR and saves in the desired location as PNG. This can be accessable through an HTML doc. | Yes | Yes
UID linkage usage shown in DVH | Yes | Not available yet
Added slider bar to scroll through selected structures in IMRTP | Yes | Not available yet
Added 3-D expansion option under “Derive New Structure” | Yes | Yes
A transverse/sagittal/coronal slice viewing program for reviewing contours, CT scans, and dose distributions. | Yes | Yes
Colorwash, transparent colorwash, or isodose line dose display. | Yes | Yes
Dose-volume and Dose-surface histogram analysis. | Yes | DVH ready, DSH not yet
Intensity Volume Histogram | Yes | Yes
Contouring/re-contouring tools. | Yes | Yes
3-D viewing of contours and dose, opaque or transparent. | Yes | Yes
Thumbnail CT navigation tool. | Yes | Yes
Dose-projection displays. | Yes | Not available yet
Dose-distance plots. | Yes | Not available yet
Dose metric comparison and subtraction tools. | Yes | WIP
Easy programmable access to all data. | Yes | Yes (Python, VTK, SimpleITK)
Registration (deformable, non-deformable) | No | Yes
Efficient memory management | No | Yes
Optimized computation & visualization performance | No | Yes
Free, open-source | yes (except Matlab) | Yes
DICOM listener | No | Yes
Large user and developer community | No | Yes
Annotations (points, ruler, ROI) | No | Yes
Multiple OS support (Windows, Linux, Mac) | Yes | Yes