## Slide 1
Acquire and build SlicerRT (on an existing Slicer)
Use python console in Slicer
Create extension and module skeletons
  Use extension template
  Use scripted module template
Next item on agenda

## Slide 2
Setting window/level values programmatically
  cd ~/Support
  python ~/Support/Slicer/Utilities/Scripts/ModuleWizard.py --template ~/Support/Slicer/Extensions/Testing/SuperBuildExtensionTemplate --target ./MyExtension MyExtension
  cd MyExtension
  python ~/Support/Slicer/Utilities/Scripts/ModuleWizard.py --template ~/Support/Slicer/Extensions/Testing/ScriptedLoadableExtensionTemplate/ScriptedLoadableModuleTemplate --target ./MyScriptedModule MyScriptedModule
Create extension skeleton
Notes: Check the directories after creating the extension template

## Slide 3
Edit super-build Cmake file
  gedit CMakeLists &
  Add under the other add_subdirectory… lines
  add_subdirectory(MyScriptedModule)
  Quit editor
  cd ..
  mkdir MyExtension_R64-bin
  cd MyExtension_R64-bin
Create extension skeleton cont’d #1
Notes: Open editor from new tab
Check the directories after creating the extension template

## Slide 4
Configure extension skeleton
  ../cmake-2.8.10.2-Linux-i386/cmake –DCMAKE_CXX_COMPILER=/usr/bin/g++-4.6 ––DSlicer_DIR=/home/slicer/Support/Slicer4-SuperBuild-Debug/Slicer-build –DMyExtension_SUPERBUILD=0 ../MyExtension
Build extension skeleton
  make
Create extension skeleton cont’d #2
Notes: Check the directories after creating the extension template
(In case it’s needed: DCMAKE_BUILD_TYPE=Release)

## Slide 5
Start Slicer
Add modules to the additional module paths
  Go to Edit / Application settings / Modules
  Click the “>>” button next to the Additional module paths section
  Add the following directories:
    ~/Support/MyExtension_R64-bin/lib/Slicer-4.2/qt-loadable-modules
    same location but the directory qt-scripted-module
Add new modules to the paths
Notes: The CLI module appears to be built in the Slicer-build directory