## Slide 1: SlicerRT Image-guided radiation therapy research toolkit for 3D Slicer
Csaba Pinter1, Andras Lasso1, An Wang2, David Jaffray2, and Gabor Fichtinger1
1Laboratory for Percutaneous Surgery, Queen’s University, Canada 2University Health Network, Toronto, ON, Canada

## Slide 2
Goal: provide open-source platform for translational clinical research, mainly cancer
Themes:
  SlicerRT: radiotherapy toolkit for 3D Slicer
  SlicerIGT: Image-guided therapy with 3D Slicer
Funding by Cancer Care Ontario till 2016
PI & co-PIs: Gabor Fichtinger (Queen’s), David Jaffray (Toronto UHN), Terry Peters (Robarts)
SparKit project overview
Notes: Runs under the umbrella project SparKit: Software Platform and Adaptive Radiotherapy Kit
Originally funded by OCAIRO, didn’t cover platform development.

## Slide 3: Motivation behind SlicerRT
Commercial treatment planning systems (TPS)
Existing research tools CERR, PLUNC, dicompyler, etc.
Expensive
Closed
Cover only routine clinical procedures
Stable
Unstable
User-friendly
Not extensible
Not flexible
Poor documentation
Large, non-modular code base
Insufficient user and developer support
Inconvenient
Well documented
Limited feature set
Flexible
Extensible
SlicerRT
Open-source
Platform-independent
Open-source?
Free
Notes: Lack of a comprehensive and open radiation therapy toolkit
RT researchers use commercial TPSs along with existing research tools. Both categories have serious shortcomings when being used for research purposes.
SlicerRT aspires to overcome these limitations, and also congregate their strong properties, such as ease of use, stability, flexibility, and so on.

## Slide 4
Development principles
Leverage existing tools and parallel efforts: 3D Slicer1, Plastimatch2
“Hub” for RT data analysis and comparison
Cover most common RT research workflows
Free, open-source license (BSD)
Open to integrate algorithms
Extensive documentation
1 S. Pieper, M. Halle, and R. Kikinis, 3D SLICER. Proceedings of the 1st IEEE International Symposium on Biomedical Imaging: From Nano to Macro (Brigham and Women’s Hospital, Boston, MA, 2004), pp. 632–635.
2 G. C. Sharp, R. Li, J. Wolfgang, G. Chen, M. Peroni, M. F. Spadea, S. Mori, J. Zhang, J. Shackleford, and N. Kandasamy, “Plastimatch: An open source software suite for radiotherapy image processing,” in Proceedings of the XVIth International Conference on the Use of Computers in Radiotherapy (ICCR) (Amsterdam, the Netherlands, 2010).
Pinnacle³
Eclipse™
SlicerRT
DICOM-RT
DICOM-RT
MATLAB
DICOM-RT
XiO®
DICOM-RT
Notes: Approach is to leverage… By doing so, we can minimize parallel developments of for example visualization or registration tools, that are otherwise crucial parts of an RT research toolkit.
We aim SlicerRT to be a hub for…The hub approach is illustrated on the right side. It shows that SlicerRT cooperates with multiple treatment planning systems and Matlab, using their native formats.

## Slide 5
SlicerRT architecture

## Slide 6
3D Slicer
RT import (DICOM)
Visualization (volumes, models, 2D/3D, etc.)
Processing (registration, segmentation, etc.)
Analysis (error metrics, measurements, image fusion, etc.)
RT-specific analysis (dose comparison, DVH, …)
RT export (DICOM, Matlab, …)
General workflow overview
SlicerRT components
3D Slicer components
Notes: This diagram explains the general workflow that SlicerRT supports.
…It is followed by the analysis of the data using both 3D Slicer and * SlicerRT tools and algorithms…

## Slide 7
Feature group: DICOM-RT import
Integrated into core DICOM import plugin mechanism
Supported data types:
  RT structure sets → Contours → Fiducial point
  RT dose map
  RT image
  RT plan: isocenter, beams
  Planning CT, MR, etc.
Standard layout after loading phantom dataset
Notes: The first step of every RT research workflow … … seamless handling and loading of the data using only the DICOM browser in 3D Slicer

## Slide 8
Importing DICOM-RT files
DICOM RT import plugin, integrated in the DICOM plugin mechanism
Examines files and creates “loadables”
  Confidence level shows how suitable the plugin is for loading that object type
Loadables appear in the list when selecting patient/study/series
Takes charge of loading when selected and load button clicked
DICOM browser window

## Slide 9
Loading RT Structure Set
Point structures → Series of points (vtkMRMLAnnotationFiducialNode objects)
Contours → Series of “ribbons,” i.e., the structure contours expanded in 3D as band surfaces (vtkMRMLModelNode objects)
The imported contours and points are organized under a hierarchy node parent
Loaded structures as ribbon models

## Slide 10
Loading RT Dose and RT Image
Dose volume → Volumetric image (vtkMRMLVolumeNode object)
  Dose unit name and value stored in attributes
RT image → Volumetric image slices (vtkMRMLVolumeNode objects)
Loaded dose volume
Notes: RT Image future plans

## Slide 11
Loading RT Plan
Isocenter points → Fiducial points (vtkMRMLAnnotationFiducialNode objects)
Beam parameters → Basic beam geometries (vtkMRMLModelNode objects)
Loaded beams (along with anatomy, dose and structures)
Notes: Future plans

## Slide 12
Patient Hierarchy (coming soon)
New concept for maintaining relationships between
  The loaded data objects in Slicer (e.g. dose and plan)
  The loaded data objects and the original DICOM files
Comes with a module
The loaded data is organized in a Patient/Study/Series hierarchy
Utilization
  DICOM-RT export
  Derived objects can inherit special metadata (e.g. dose unit)
  Bind RT and non-RT data together (e.g. isodose sets, color tables and dose volumes)
  Transform whole studies at the same time
  Set up more advanced visualization automatically
  Show/hide complete branches

## Slide 13
Feature group: Contour analysis
Contours module: Multiple representations (automatic conversion)
  Ribbon model
  Rasterized volume
  Closed surface model
Contour morphology
  Expand, shrink
  Combine using logical operators
Contour comparison
  Dice coefficient
  Hausdorff distance

## Slide 14
Contours module
Multiple representations (automatic conversion)
  Ribbon model
  Rasterized volume
  Closed surface model
Rasterized volume
Ribbon model
Closed surface
Contours module UI
Notes: Contours module allows easy handling of the imported structure set contours, by offering multiple representations and automatic conversions between those. The supported representations are…
…the desired input format for numerous processing and analysis techniques

## Slide 15
Contour Morphology module
Expand, shrink
Combine using logical operators
Contour Morphology module UI
Target volume expanded

## Slide 16
Contour Comparison module
Hausdorff distance
Dice coefficient
Contour comparison module UI

## Slide 17
Feature group: Dose analysis
Dose volume histogram (plot visualization + metrics)
Dose accumulation
Dose comparison (gamma)
Isodose contours / surfaces
Proton dose computation
Registration
  BSpline registration
  Landwarp registration

## Slide 18
Dose Volume Histogram module
Dose Volume Histogram module UI
DVH with standard four-up quantitative layout
Compare dose volume histograms

## Slide 19: Dose metrics
Available metrics:
Total volume
Min, max, mean dose
V metrics: for user-defined levels, results in cc and %
D metrics: for user-defined levels in cc and %
Values can be exported to CSV file for further analysis.
DVH metrics in Dose Volume Histogram module

## Slide 20
Dose Accumulation module
Dose Accumulation module UI

## Slide 21
Isodose module
Isodose contours and surfaces
Computes
Isodose lines
Isodose surfaces
Isodose module UI

## Slide 22
Dose comparison module
Provides gamma dose comparison
Dose Comparison module UI
Gamma volume

## Slide 23
Plastimatch modules
Modules provided by the Plastimatch library
Proton dose computation (coming soon)
Registration
  BSpline deformable registration
  LANDWARP landmark deformable registration
  XFORMWARP Warping with transform

## Slide 24
Software quality
Extensive automatic testing done on multiple platforms every night
Validated against other software packages (Pinnacle, CERR, …)
Automatic test infrastructure for automatic verification and validation
Test results reported to the web-based dashboard
http://slicer.cdash.org/index.php?project=Slicer4
Notes: The quality of our software, which means stability, reliability, accuracy, flexibility, extensibility and maintainability is ensured by following the strict and proven development processes we adapted, and the verification and validation performed by the automated testing system. The automated unit and application tests run …
The reliability and accuracy of the SlicerRT algorithms are ensured through a series of validation tests, in course of which our results are compared to the results of other software packages, such as Pinnacle or CERR.

## Slide 25
Example use case
Import, load and visualize data
Use case: Evaluate the effectiveness of RT plan adaptation
Compute and display DVH for all methods
Register day 1 CT with day 2 CT
  Rigid
  Bspline
Resample day 2 dose using results
Accumulate doses
Compare DVH curves and metrics for target volume and organs at risk
Notes: …example use case, possibly the one that covers the most features available in SlicerRT at the moment. …
We compute the results without adaptation as a baseline. …
… between the two CT images. We need to register them and apply the registration result to the day two dose distribution, thus aligning the two datasets together for analysis.
Zooming in on the area the target dose starts to fall, we can compare the delivered dose better for each case.
We can also check the basic metrics and compute more complicated ones to quantify the differences.

## Slide 26
Collection of RT-specific modules, includes
Distributed as a 3D Slicer extension: can be downloaded, installed, upgraded using the extension manager in Slicer
SlicerRT extension for 3D Slicer
SlicerRT extension in the 3D Slicer app store (free)
Notes: SlicerRT is distributed as a 3D Slicer extension. It can be easily found and installed from the Slicer AppStore.

## Slide 27
Next steps
Enhancements planned for the next 6 months:
Patient Hierarchy
DICOM-RT export
Matlab bridge interface: execute Matlab functions from 3D Slicer
Digitally reconstructed radiograph
Support CERR PlanC format
Scripting examples
More testing and validation
Detailed plan: https://www.assembla.com/spaces/slicerrt/tickets
Current radiotherapy modules (including work-in-progress modules)
Notes: Suggestions, comments and feature requests are warmly welcome! Our weekly meetings on every Monday are also open to anybody to discuss any matter related to the toolkit.

## Slide 28
Thank you!
Overview paper: Csaba Pinter, Andras Lasso, An Wang, David Jaffray, and Gabor Fichtinger, “SlicerRT: Radiation therapy research toolkit for 3D Slicer”, Med. Phys. 39 (10), October 2012
Project homepage: http://www.SlicerRT.org/
Contact: Csaba Pinter (pinter@cs.queensu.ca)