## Slide 1: Performing radiation therapy research using the open-source SlicerRT toolkit
Csaba Pinter1, Andras Lasso1, An Wang2, Gregory C. Sharp3, Kevin Alexander4, David Jaffray2, and Gabor Fichtinger1
1Laboratory for Percutaneous Surgery, Queen’s University, Kingston, ON, Canada 2University Health Network, Toronto, ON, Canada
3Department of Radiation Oncology, Massachusetts General Hospital, Boston, MA, USA
4Department of Physics, Eng. Phys., and Astrophysics, Queen’s University, Kingston, ON

## Slide 2
Bringing ideas and tools together
http://SlicerRT.org
Pinnacle³
Eclipse™
XiO®
DICOM-RT
Routine
Research
Data transfer
Conversions
2D/3D visualization
Dose analysis
Contour analysis
Segmentation, Registration
...
...

## Slide 3
Development principles
Based on consensus discussions with RT researchers
Cover most common RT research workflows
Leverage existing tools: 3D Slicer, Plastimatch
Free, open-source license (BSD)
  Open to integrate algorithms
  Contribute back to community
High quality software, developed using industrial standards
G. C. Sharp et al. 2010
S. Pieper et al. 2004
SlicerRT dashboard, performing automatic testing every night

## Slide 4
3D Slicer
Medical image analysis and visualization platform
Since 1997
$50M in funding (>2,000 years of labor)
Professionally engineered
1,000+ analysis functions
200K downloads for 4.4
www.slicer.org
3D Slicer downloads

## Slide 5
SlicerRT ecosystem
3D Slicer
Utilities
Streamlined applications
SlicerRT core
Several former SlicerRT features integrated:
Subject hierarchy, DICOM export, Transform visualizer, etc.
Common RT software tools:
DICOM-RT, Dose/Contour analysis, Beam planning, Batch processing
Acts as a platform

## Slide 6
Example use case: Image-guided RT
Determine daily displacement
Evaluate dosimetric improvement (DVH, gamma)
Export patient setup correction
Collaboration with PMH, Toronto
Dosimetric improvement after patient setup correction

## Slide 7
Example use case: Dose accumulation
Register anatomical images
Transform whole studies
Accumulate dose
Compute DVH
Collaboration with PMH, Toronto
Pinter et al., MedPhys, 2012
Evaluate plans using DVH
Visualize transforms, anatomy in 3D
Convenience features: Transform whole studies with a single click

## Slide 8
Example use case: Proton dose calculation
External beam planning
  Arbitrary dose engines
  Using same user interface
  Potentially replace TPS
Evaluate plan
Export plan for delivery
Collaboration with MGH, Boston and CRO, Italy
Desplanques et al., MedPhys, 2014
Poster at World Congress: PS04.087

## Slide 9
Example use case: SlicerRT in the cloud
Highly parallel computations
Very large amount of data
Self-driven RT scripts
Scripted analysis
Local control
Feasibility study: Find most similar daily plan from a database of plans
  Initialize daily ART plan from most similar one
Andrea et al., ImNO 2015 Talk at World Congress: SP130.6

## Slide 10
Example use case: Use custom MATLAB algorithm
Make MATLAB algorithms easier to use
Integrate into workflow
Rely on the power of SlicerRT and 3D Slicer
No programming
Collaboration with KGH, Kingston, ON
Alexander et al., AAPM 2015
DICOM-RT
Non-DICOM

## Slide 11
Example use case: Gel dosimetry analysis
Full 3D gel dosimetry
Simplified user interface
Collaboration with KGH, Kingston, ON
Alexander et al., IC3DDose, 2014
Talk at World Congress: SP057.3

## Slide 12
Extensions for 3D Slicer
SlicerRT extension in the 3D Slicer app store (free)
Downloads (for version 4.4)
3D Slicer: ~200,000
SlicerRT: ~750
Matlab Bridge: ~330
All other extensions: less than 300
Notes: SlicerRT is distributed as a 3D Slicer extension. It can be easily found and installed from the Slicer AppStore.

## Slide 13
Thank you for your attention!
csaba.pinter@queensu.ca
http://SlicerRT.org
Please join our weekly “SlicerRT clinic” meetings

## Slide 15
Appendix

## Slide 16
SlicerRT core highlights
Armed with the full power of 3D Slicer
DICOM-RT
Multi-fraction data handling
registration
Load and visualize DICOM-RT
Advanced visualizations
Multi-fraction data view

## Slide 17
SlicerRT core highlights
Contour analysis
  Multi-representation support
  Morphological operators
  Comparison methods
Dose analysis
  DVH calculation, comparison
  Gamma dose comparison
  Dose accumulation
  Isodose surfaces
  External beam planning platform
External beam planning
Contour representations
Dose-volume histogram

## Slide 18
Matlab bridge
Running Matlab functions directly from 3D Slicer
Takes input from the data loaded into Slicer
  Transfers and shows the results in Slicer when MATLAB execution is completed
GUI is generated automatically from a standard command-line interface definition XML file
  no GUI programming needed
No building of 3D Slicer or MEX files, etc. are needed

## Slide 19
Sequences
Create and visualize of higher-dimension data nodes
  RT: Multi-fraction datasets, 4D CT
Sequence browser for selection and playback
Synchronized or real-time visualization
  In 2D and/or 3D
Handling of whole fraction dataset in each sequence node
Playback of a 4D cardiac CT dataset

## Slide 20
Radiation therapy challenges
Research
Routine
Adaptive RT
Image-guided RT
Treatment planning
3D Dosimetry
Novel radiation protocols
Computational methods
Image registration
Image segmentation
Fractionation data management
Image/contour comparisons
Outcome prediction
Knowledge-based RT
?

## Slide 21: Translational research
Commercial treatment planning systems (TPS)
Existing research tools CERR, PLUNC, dicompyler, etc.
Expensive
Closed
Cover only routine clinical procedures
Stable
Unstable
User-friendly
Not extensible
Not flexible
Poor documentation
Large, non-modular code base
Insufficient user and developer support
Inconvenient
Well documented
Limited feature set
Flexible
Extensible
SlicerRT
Open-source
Platform-independent
Open-source?
Free